## Slide 1: TCEQ Air Monitoring Quality Assurance Overview
Texas Commission on Environmental Quality
Stephanie Ma, Ambient Monitoring Section Manager

## Slide 2: The Texas air monitoring network consists of roughly 230 monitoring stations with over 500 individual pollutant samplers. Over half of the network is owned and operated by the TCEQ.

## Slide 3: Compounds of Interest
Six criteria pollutants:
  Ozone
  Carbon monoxide
  Nitrogen Dioxide
  Sulfur Dioxide
  Lead
  Particulate matter
    Particulate matter less than 10 micrometers in diameter (PM10)
    Particulate matter less than 2.5 micrometers in diameter (PM2.5)
Robust network of state-initiative monitoring that also includes:
    Volatile organic compounds (VOCs)
    Hydrogen sulfide

## Slide 4: Quality Assurance Overview
Quality system implementation
Siting criteria
Monitoring equipment
Data validation
Audits

## Slide 5: Quality System Implementation
Quality Management Plan
Quality Assurance Project Plans
Standard Operating Procedure (SOPs)
Personnel Qualifications and Training
Documentation
Notes: Operator logs and chain of custody forms
Quality control records
Data validation records
Training Records

## Slide 6: Siting Criteria – evaluated during initial site selection and annually thereafter
Sampler monitoring objective
Parameter specific
Federal siting criteria requirements
Distance from trees, obstructions, and roadways
Unrestricted air flow
Probe height and material

## Slide 7: Monitoring Equipment
TCEQ uses federal reference method (FRM) or federal equivalent method (FEM) monitoring equipment for criteria pollutants
Equipment must be operated according to the manufacturer’s specifications
  Preventive maintenance
  Operating conditions such as temperature and humidity
  Quality control (QC) checks
    Flow checks
Equipment comparisons and test plans

## Slide 8: Field Quality Control Checks
Automated daily, weekly, and monthly checks on the continuous gaseous analyzers
Calibrations and monthly verification checks for PM equipment

## Slide 9: Data Validation
QC data review
  Bracketing data
Cross-site comparisons
Identifying anomalies
Site documentation

## Slide 10: Audits
Field audits
  Flow, temperature, and pressure audits
  Laboratory control checks
Performance evaluation (PE) audits
Technical systems audits

## Slide 12: Questions?
Stephanie Ma, Manager
  Ambient Monitoring Section
  512-239-6256
  Stephanie.ma@tceq.texas.gov