## Slide 1
New Chemical Approaches for
Air Quality Modeling
– TCEQ Presentation August, 22, 2023 –
William R. Stockwell
Rosa M. Fitzgerald
University of Texas at El Paso

## Slide 2
Brain
Lungs
Heart
O3, PM2.5 PM10
Why Do We Care?
Ozone and Particulate Matter (PM2.5 and PM10) are inhaled.
O3 may inflame lung linings.
PM2.5 may lodge in the lungs and may travel to the heart and brain where they can cause more damage.
2

## Slide 3
The Atmospheric System
3

## Slide 4
Eulerian Grid Models for Air Quality
Numerical Complexity Increases with Number of Modeled Pollutants
A Very Large Number of Grid Boxes
4

## Slide 5
Air Quality Model Modules
5

## Slide 6: Tropospheric O3 Chemistry
Sun
O3 Formation
NO2 + h  O(3P) + NO
O(3P) + O2 (+ M)  O3 (+ M)
Ozone Destruction
NO + O3  NO2 + O2
Steady-State Ozone Concentrations
d[NO]/dt = J[NO2] - k[NO][O3]  0
[O3] = {J / k} {[NO2] / [NO]}
6

## Slide 7
Tropospheric Ozone Concentrations
for Air Polluted by NO and NO2 Only.
7

## Slide 8: HO Radical Production
O3 + h  O(1D) + O2
O(1D) + N2  O(3P) + N2
O(1D) + O2  O(3P) + O2
O(3P) + O2 (+ M)  O3 (+ M)
O(1D) + H2O  2 HO
Sun
8
8

## Slide 9: Alkane Oxidation
HO + CH3CH3  H2O + CH3CH2
CH3CH2 + O2  CH3CH2O2
CH3CH2O2 + NO  CH3CH2O + NO2
CH3CH2O + O2  CH3CHO + HO2
HO2 + NO  HO + NO2
Conversion of NO to NO2 produces O3
9

## Slide 10
Photolysis of Ozone, Nitrogen Dioxide and Reactions of Organic Gases are Key to Ozone and Aerosol Production
h
h
Inorganic
Aerosol
+ NH3
+ SO2
Aq. Chem
Secondary
Organic Aerosol
10

## Slide 11: NOx and VOC Dependence
11

## Slide 12
26-Fullerene
Soot and Secondary Organic Aerosol (SOA)
are Major Health Concerns
Soot
Note the similarity to carbon nanostructures.
Polanco, Ramos, Fitzgerald and Stockwell, An Improved Method for Optical Characterization of Mineral Dust and Soot Particles at the El Paso-Juárez Airshed, Atmosphere, 11, 866, 2020. https://doi.org/10.3390/atmos11080866
Computational Models of Soot
Note reactive sites (Red and Blue) that may influence health effects.
12

## Slide 13: Eulerian Air Quality Models, Meteorology and Processes
Examples of Widely Used Models
Meteorological Models
WRF: Weather Research
& Forecasting Model
Emissions Modeling Platforms
SMOKE: Sparse Matrix Operator Kernel Emissions
Air Quality Models
CMAQ: The Community Multiscale
Air Quality Modeling System
CAMx: Comprehensive Air Quality
Model with Extensions (CAMx)
WRF-Chem
Health / Ecomomic Effects Models
BINMAP-CE: Environmental Benefits Mapping and Analysis Program - Community Edition (BenMAP-CE)
13

## Slide 14
Balance the Treatment of
Meteorological and Chemical Processes in Eulerian Air Quality Models
Use Practical Mechanisms for Modeling Air Quality
Use complete enough chemistry to describe the air quality situation but multi-million reaction mechanisms will not improve the accuracy of air quality simulations.
Multi-Phase Chemistry
A closer coupling of gas-phase and aerosol processes in models should improve gas-phase & secondary particulate matter simulations.
14

## Slide 15
1990
Regional Acid Deposition Mechanism, version 2 (RADM2)
15
1997
Regional Atmospheric Chemistry Mechanism (RACM)
2013
Regional Atmospheric Chemistry Mechanism, version 2 (RACM2)
2023
Community Regional Atmospheric Chemistry Multiphase Mechanism (CRACMM)
RADM / RACM / CRACMM Series
Expected to Become CMAQ Default

## Slide 16
RADM / RACM / CRACMM
Series Design Philosophy
16
Provide a more detailed description of background and low NOx atmospheric chemistry than available in urban scale mechanisms during the early 1980s. Example: avoid operator approaches to peroxy-radicals.
Multi-day scenarios need to be simulated. Day/Nighttime chemistry important.
Limit VOC detail to describe VOCs in the emissions inventories. Why have many more stable VOC species in the mechanism than available in the inventory?
Provide a chemical mechanism compact enough (numbers of reactions and species) so that it can run in Eulerian Air Quality Models. But size may range toward the upper bound.
Use sensitivity and uncertainty analysis as guides in mechanism development.

## Slide 17
New CRACMM
New CRACMM in CMAQ vs Older Mechanisms
17
CRACMMv1.0 Average Summer O3
CRACMMv1.0 – CB6r3 Average O3
CRACMMv1.0 – RACM2 Average O3
Average O3 Concentration (ppb)
16 20 24 28 32
Average O3 Difference (ppb)
Average O3 Difference (ppb)
-4 -2 0 + 2 +4
-4 -2 0 + 2 +4

## Slide 18
New CRACMM
Example of Using Models to
Evaluate Control Stratagies
The Los Angeles South Coast Air Basin
18

## Slide 19: Key Research Questions for Coordinating Research Council Los Angeles Study
New CRACMM
The California Air Resources Board (ARB) and the South Coast Air Quality Management District (SCAQMD) have developed Emissions Reduction Plans for the South Coast Air Basin (SoCAB) to reduce Ozone and Particulate Matter Concentrations by the year 2030.
The plan focuses heavily on the reduction of nitrogen oxide (NOx) emissions.
Will the plan work for Particulate Matter?
The Community Multi-scale Air Quality model was used to simulate two high PM episodes for 2008 and 2030.
19

## Slide 20
New CRACMM
Simulated 24-hr Average PM2.5
November 20, 2008 – Aerosol Season, Example Day
Micrograms m-3
20

## Slide 21
New CRACMM
CMAQ Simulated 24-hr average PM2.5 Concentrations SoCAB November 20, 2030 – Aerosol Season
Planned NOx Reductions
21

## Slide 22
New CRACMM
Simulated particulate matter mass concentrations by component for 2008 and 2030 – Anaheim
Concentration m-3
Anaheim
22
Anthropogenic SOA
Primary Organic Matter
Elemental Carbon
Biogenic SOA
Ammonium Nitrate
Ammonium Sulfate
Unidentified PM2.5
Course Mass

## Slide 23
New CRACMM
SoCAB Health
and
Economic Effects
Environmental Benefits Mapping and Analysis Program – Community Edition
23

## Slide 24
New CRACMM
Change in exposed population between base case and future-year control year case.
Change in
adverse health effects incidence.
Economic value of change in air quality.
Results: Maps, Tables, etc.
Change in air quality
Difference between base case and future-year control case.
Determine Air Quality Surfaces
Health Impact Calculations
Incidence Rates
Health Impact Functions
Economic Cost and Benefits
Reporting
Valuation Functions
Steps and the input data files required to run BenMAP-CE.
Base case
Control case
24
Population Data

## Slide 25
New CRACMM
Estimated Avoided PM2.5 Related 2030 Mortalities for Six VOC and NOx Emission Reduction Scenarios in the SoCAB
25

## Slide 26
New CRACMM
Total monetized health benefits for all avoided PM2.5 related health impacts for the six VOC and NOx emission reduction scenarios in the SoCAB region.
26

## Slide 27
New CRACMM
SoCAB Air Quality Model Simulation Conclusions
Ammonium nitrate was the most abundant secondary aerosol component and its production is a very nonlinear function of both NOx and VOC emissions.
The emissions control strategy of the California Air Resources Board reduces PM2.5 exposure and would save $6.6 Billion dollars compared with 2008.
But the 2030 target emissions control strategy is the least effective in reducing PM2.5 concentrations and improving health of the six future-year cases simulated.
Published: Stewart, D.R., E. Saunders, R. Perea, R. Fitzgerald, D.E. Campbell, W.R. Stockwell, J. Air and Waste Management Association, 69, 192–208, 2019.
Stewart, D.R., E. Saunders, R.A. Perea, R. Fitzgerald, D.E. Campbell and W.R. Stockwell, Environmental Health Insights, 11, 1-13, 2017.
27

## Slide 28
28
A Diverse and Balanced Community
Maintain a diverse community of scientists. Diverse in terms of sex, race, culture and scientific discipline (e.g. more applied mathematicians are desperately needed).
A diverse community should provide new approaches and provide an important check on mainstream trends. – Reduce groupthink.
Greater mixing between atmospheric chemists, air quality modelers and policy makers would encourage greater balance in all three areas.

## Slide 29
Acknowledgement
29
Thank You for Your Support!